## Slide 1: Connected Work Zone Software Toolchain
Work Flow and Current Progress
Niraj Vasant Altekar
04/25/2019

## Slide 2: Outline
Process Flow
Pre-requisites
Configuration
CAMP Software Tool Chain - Flow
Data collection
Work Zone configuration
Map Builder
Map Visualizer
Other Observations and Notes

## Slide 3: Process Flow
Initial Configuration 
CAMP Software Toolchain
  Vehicle Path Data Acquisition  (.csv) 
  (.csv)  Work Zone Configuration  (.wzc) 
  (.wzc)  Map Builder  (.xml) 
  Map Visualizer 
  (.xml)  RSM Message Builder  (.uper) 
(.uper)  Deployment on the RSU through RSU4.1 Interface
Processing on OBU

## Slide 4: Pre-requisites
Hardware:
  External computer for data collection and message development.
  U-Blox EVK-M8N GNSS Evaluation Kit for receiving GPS data.
Software (External Computer) :
  Python
  U-Center v8.25
  CAMP Connected work zone software toolchain

## Slide 5: Physical Connections
GPS Receiver
U-Blox GNSS Evaluation Kit
External Computer

## Slide 6: Configuring U-Blox GPS Receiver
Install U-blox supplied u-center software (v8.25)
Connect GPS receiver with supplied USB cable to a USB port on PC. (Virtual serial port connectivity)
Launch the u-center application.
To setup baud rate for serial communication: a. Select Receiver  Port – Note down the virtual serial port number. This port number will be used by the Vehicle Path Data Acquisition tool.
Select Receiver  Baud rate  115200
To apply configuration file: ALL_CAMP_V2V_MD_UbloxM8N-10Hz_GPS_Only_Config_v1.2.txt located in U-blox EVK M8N folder in the toolchain distribution package
  Select Tool  GNSS Configuration
  Select and apply the configuration file

## Slide 7: CAMP Software Toolchain - Flow

## Slide 8: Data Collection on 03/28/2019 33.435425, -112.293444 to 33.437068, -112.225599
MC85/S-107th Avenue to MC85/S-75th Avenue (4.0 Miles)
One Round Trip (12:00PM – 01:00PM)
Data Captured: (.csv)
  GPS waypoints, lane closures, presence of workers, locations of RSUs

## Slide 9: Data Collection on 03/28/2019 33.435425, -112.293444 to 33.437068, -112.225599
Data collected in (.csv) format
# of Data Points: 4641

## Slide 10: Work Zone Configuration

## Slide 11: Map Builder - Info

## Slide 12: Map Visualizer

## Slide 13: Data Collection on 04/19/2019 33.4631175, -112.1335158 to 33.46284333, -112.2274112
I-10/35th Avenue to I-10/75th Avenue (5.0 Miles)
One Round Trip (2:30PM – 3:30PM)
Data Captured: (.csv)
  GPS waypoints, lane closures, presence of workers, lane merges

## Slide 14: Questions (1)
Is data collection required for each change in the work-zone?
  Changes in the message required as the configuration of the work-zone changes
  For example, When lane closure/opening points change
  Presence of workers is highly time dependent
  Would data collection be required for each change?
  If yes, any suggested guidelines to standardize the data collection process?

## Slide 15: Questions (2)
Use Case: Dedicated left (or right) turn lanes in the vicinity of the intersections?
Use Case: Additional (dynamic) number of short lanes, not necessarily in the vicinity of the intersection.

## Slide 16: Questions (3)
Use Case: Usage of bidirectional-shared lane?
Use Case: Closure of all lanes and opening a new lane altogether (merging into bi-directional lanes) – Ambiguity during data collection.

## Slide 17: Questions (4) - Freeway
Use Case: On freeways (refer I-10 data collection), the lanes that merge into exit ramp or merge from entry ramp.
Use Case: Dynamic changes in lane width.
Use Case: Considering HOV lane.
Use Case: Shoulder closures
Use Case: Variable speed limits within the work-zones.
General Use Case: ​UPER->XML decoding and XML->uper encoding of CV messages other than RSM, using the CV-message builder.

## Slide 18: Other Observations and Notes
Savari SW1000 supports only TIM message for the store-repeat application.
  However, we can forward the RSM message to the RSU for broadcast through RSU4.1 Interface
  DSRC MsgID: 33
RSM message is highly flexible to include address many other roadside conditions such as:
  School Zone Warnings
  Rail Road Warnings
  Weather/Road Conditions
  Vehicle Breakdowns
  Emergency Vehicle Alert
  Reference: Connected Vehicle Message Builder User Guide v1.4
A general OBU application can be developed to address the probable conditions.