## Slide 1: Multi Modal Intelligent Traffic Control in a Connected Vehicle Environment
Niraj Vasant Altekar
May 17, 2019

## Slide 3
Advanced traffic signal controls based on traffic flow
Transit/Freight vehicles leveraging signal priority
Data collected from connected vehicles provide insights into the performance of the intersection
Interconnected Pedestrians Mobility Application - Disabled pedestrians make their way safely through intersections
Prioritization of Emergency vehicles

## Slide 4: Road Intersection Terminology
Phase Numbering
  NEMA Conventions
  Odd: Left Turn Movements
  Even: Through Movements
  Clockwise 3-8-1-6-7-4-5-2
Approach Numbering
  Odd: Ingress
  Even: Egress
  Anticlockwise 1-2-3-4-5-6-7-8
Vehicle Detectors
Signal Heads
2
1
3
4
5
6
7
8
#
Approach

## Slide 5: Signal Control
Fixed Time Signal Control
  Signal times are predetermined for all phases
  May have different timing plans for different time of the day to accommodate traffic volume variations
Traffic Actuated Signal Control
  Signal times are determined based on traffic demand in real-time.
  3 Important time values:
    Minimum Green (Gmin)
    Vehicle Extension (Ext) or Passage Time
    Maximum Green (Gmax)
  When a vehicle is detected, a call for green is placed for a phase. Signal remains green for minimum green time.
  Green time is extended to accommodate the demand until maximum green time is reached.
  Criteria for phase termination (end of green time)
    Gap out : No more vehicles detected within the Vehicle extension time
    Max out : Maximum green time reached

## Slide 6: Ring Barrier Logic
1 | 2 | 3 | 4
5 | 6 | 7 | 8
Ring-1
Ring-2
Time
Barrier

## Slide 7: Signal Controller - Interface
Simulation Time
Serving Phases
Phase Current Status
Vehicle Calls
Gmin or Ext Timer
Max Green

## Slide 8: System Simulation – Basic System
Simulation Resolution: 10 Real Time steps/Simulation Second
Normal Traffic Actuated Signal System
Trucks enters the network at 00:01:50 (Simulation time), and enters the visible section at 00:01:57.
Truck reaches intersection at Red (Phase 2) and spends 18 simulation seconds (180 real seconds) at the intersection.
This is due to continuous green extension on phases 4 and 8.
Phase termination Criteria for 4 & 8: Max Out
3
8
1
6
7
4
5
2

## Slide 9: Connected Vehicle Environment
Pedestrian to Vehicle
Vehicle to Vehicle
Pedestrian to Infrastructure
Vehicle to Infrastructure

## Slide 10: Connected Vehicle Messages
Broadcast by Vehicle
  BSM (Basic Safety Message) - 10 messages per second
  Vehicle position, speed, heading, acceleration, braking status, etc.
Broadcast by Infrastructure
  SPaT – Signal Phase and Timing
  MAP – Digital Map of the Intersection
  Intersection Specific Messages - Weather conditions, incident warnings, etc.
Priority Requests
  SRM – Signal Request Message
  SSM – Signal Status Message

## Slide 11: System Simulation – Freight Signal Priority
Simulation Resolution: 10 Real Time steps/Simulation Second
Normal Traffic Actuated Signal System
Trucks enters the network at 00:01:50 (Simulation Time). And starts sending signal request messages.
Before truck reaches the intersection, phases 4 and 8 are “forced off” after their Gmin, to give priority to Truck.
Observe Gmax counter for phases 4 and 8 at 00:02:03 (Simulation time)
The controller resumes the normal operations after the truck leaves.
Phase termination Criteria for 4 & 8: Force Off
3
8
1
6
7
4
5
2

## Slide 12
MMITSS Software Architecture

## Slide 13: Simulation Platform Architecture
SIL/CID
OBE
#1
OBE
#2
OBE
#m
Signal Controller
RSE
#n
driverModel.dll
Ethernet or
DSRC (5.9 GHz)
[SAE J2735]
Ethernet - NTCIP 1202
VISSIM x-y plane to GPS (WGS - 84)
Vehicle Position Mapping
In-Vehicle Display
(HIL)
RSE
#n
RSE
#n
GID#n
GID#n
GID#n
VISSIM
OBE
Distributor
MMITSS

## Slide 14: Arizona Connected Vehicle Test Bed
DSRC Installations:
11 Signalized Intersection
6 Freeway Interchanges1
Freeway Locations1
Approx. 25,000 Residents
Approx. 10,000 Vehicles
1 2017 Expansion Project (ADOT)